## Slide 1: Confidentiality
By participating in this event, you are agreeing not to use the presented information for purposes unrelated to the event until approved by SRC;
You may hear material that represents current research, some of which has not been published or protected. This material is not for public disclosure and until potential IP rights have been protected, please treat all of the information presented as confidential information which is the property of the researcher and their university.
1

## Slide 2: SRC Task ID: 3173.001 Standardizing Boolean Transforms to Improve Quality and Runtime of CAD Tools
2
Alan Mishchenko
Department of EECS
UC Berkeley
SRC Select Disclosure
Notes: 2

## Slide 3: Task Overview
3
SRC task ID: 3173.001
Start date: January 1, 2023
Thrust area: CADT
Task leader:
  Alan Mishchenko, Univ. of California/Berkeley
Industrial liaisons:
  See next slide
Students:
  Yukio Miyasaka (graduating in 2024)
SRC Select Disclosure
Notes: 3

## Slide 4: Industrial Liaisons
4
IBM
  Victor Kravets
  Gi-Joon Nam
Intel
  Vivek Rajan
  Michael Kishinevsky
Siemens
  Attila Jurecska
  Sagar Chaki
AMD
  Aman Gayasen
  Yuji Kukimoto
Texas Instruments
  Devanathan Varadarajan
  Venkatraman Ramakrishnan
SRC Select Disclosure
Notes: 4

## Slide 5: Academic Collaborators
Discuss, publish, exchange visits with:
  EPFL, Switzerland (group of Professor G. De Micheli)
  Tokyo University, Japan (group of Professor M. Fujita)
  NTU, Taiwan (group of Professor R. Jiang)
  UMass, Amherst (group of Professor M. Ciesielski)
  UFRGS, Brazil (group of Professor A. Reis)
  Ritsumeikan University, Kyoto, Japan (group of Professor S. Yamashita)
SRC Select Disclosure

## Slide 6: Anticipated Results
6
This proposal addresses the need for powerful and scalable, yet versatile and reusable Boolean logic transforms and transform solvers, capable of solving complex synthesis and verification tasks, for any implementation technology, with predictable runtime that is close to linear in the design size.
SRC Select Disclosure
Notes: 6

## Slide 7: Task Deliverables
7
Year 1:
Documented unified representation format for individual instances of circuit synthesis problems coming from different applications. Several representative suites of practical benchmarks. An early version of Boolean transform solvers applicable to the benchmarks in the given format (Software, Report) [12/31/23]
Year 2:
Software release of the improved versions of three Boolean transform solvers: (1) fast truth-table-based circuit rewriting, (2) high-effort SAT-based area optimization, and (2) large-scale circuit restructuring. Evaluation on industrial problems (Software, Report) [12/31/24]
Year 3:
Multicore versions of the Boolean transform solvers, integrated with a number of application packages, including circuit rewriting, post-mapping don’t-care-based optimization resynthesis, and reverse-engineering. Evaluation on industrial problems (Software, Report) [12/31/25]
https://app.pillar.science/projects/5111/overview
SRC Select Disclosure
Notes: 7

## Slide 8: Background
8
Modern CAD tools transform digital designs expressed using hardware description languages into circuits realizable in FPGA, ASIC, or one of the novel implementation technologies. Another key task solved by the tools is verifying the results of synthesis. The efficiency of synthesis and verification depends not only on the design type and size, technology, and the runtime budget, but also on the generality and expressive power of the Boolean transforms used in the tools.
The Boolean transforms are understood in this proposal as operations solving individual instances of the central problem of logic synthesis: given a Boolean function and a set of divisors, find a small enough circuit to implement the function. (When there is no initial circuit, the divisors are the primary inputs.)
Boolean transforms (such as decomposition and resubstitution) are distinguished from synthesis engines (such as critical path resynthesis or post-mapping area optimization). Dedicated solvers realize Boolean transforms and are used to build synthesis engines integrated into modern CAD tools. Thus, standardizing Boolean transforms helps develop versatile transform solvers, which enable efficient next-generation tools for synthesis and verification.
SRC Select Disclosure

## Slide 9: Progress Summary
9
1st year: (1) Representation format for individual instances of circuit synthesis problems. (2) Several suites of benchmarks. (3) An early version of Boolean transform solvers applicable to the benchmarks in the given format.
  Developed a representation format and collected benchmarks
  Developed several prototype solvers
  Have shown significant QoR improvements
2nd year: Software release of the improved versions of three Boolean transform solvers
3rd year: Multicore versions of the Boolean transform solvers, integrated with a number of application packages
SRC Select Disclosure

## Slide 10: Comparison
10
Traditional AIG rewriting
  A. Mishchenko, S. Chatterjee, and R. Brayton, "DAG-aware AIG rewriting: A fresh look at combinational logic synthesis", Proc. DAC '06, pp. 532-536.
Resubstitution with don’t-cares
  A. Mishchenko, R. Brayton, J.-H. R. Jiang, and S. Jang, "Scalable don't care based logic optimization and resynthesis", Proc. FPGA'09, pp. 151-160.
Area optimization based on variable reordering
  Y. Miyasaka, A. Mishchenko, J. Wawrzynek, and N. J. Fraser, "Synthesizing practical Boolean functions using truth tables", Proc. IWLS'22.
SRC Select Disclosure

## Slide 11: Research Overview
11
Representation format
Prototype solvers
  SAT-based exact synthesis
  Boolean decomposition-based restructuring
  The new transduction-based area optimization
Experimental evaluation
SRC Select Disclosure

## Slide 12: And-Inverter Graph (AIG)
cdab | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 0
01 | 0 | 0 | 1 | 1
11 | 0 | 1 | 1 | 0
10 | 0 | 0 | 1 | 0
F(a,b,c,d) = ab + d(ac’+bc)
F(a,b,c,d) = ac’(b’d’)’ + c(a’d’)’ = ac’(b+d) + bc(a+d)
cdab | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 0
01 | 0 | 0 | 1 | 1
11 | 0 | 1 | 1 | 0
10 | 0 | 0 | 1 | 0
6 nodes
4 levels
7 nodes
3 levels
b
c
a
c
a
b
d
a
c
b
d
b
c
a
d
AIG is a Boolean network composed of two-input ANDs and inverters.

## Slide 13: BLIF Format
Onset minterms:
.names a b c d F
0011 1
0111 1
1011 1
1111 1
1100 1
1101 1
1110 1
Onset cubes:
.names a b c d F
--11 1
11–- 1
Circuit representation:
.names a b n1
11 1
.names c d n2
11 1
.names n1 n2 F
-1 1
1- 1
a
b
c
d
F = ab + cd
Drawbacks:
Not easy to represent don’t-cares
Does not work for Boolean relations

## Slide 14: Proposed Format
A problem w/o don’t-cares:
4 0 1 16
0101010101010101
0011001100110011
0000111100001111
0000000011111111
1110111011100000
0001000100011111
Solution:
2 4 6 8 11 13 15 15
A problem with don’t-cares:
4 0 1 5
00-1-
--01-
0-0-1
-0--1
11100
00011
a
b
c
d
F = ab + cd

## Slide 15: Proposed Format
A problem w/o don’t-cares:
4 0 1 16
0101010101010101 // a
0011001100110011 // b
0000111100001111 // c
0000000011111111 // d
1110111011100000 // ~F
0001000100011111 // F
Solution literals:
(2 4) (6 8) (11 13) (15 15)
Literal = 2*NodeN + Compl
A problem with don’t-cares:
4 0 1 5
00-1- // a
--01- // b
0-0-1 // c
-0--1 // d
11100 // ~F
00011 // F
a
b
c
d
F = ab + cd
Node0 is the Const0 node
Node1 … Node4
Node5
Node6
Node7
Node5
Node6
Node7
Output node

## Slide 16: Prototype Solvers
Developed several prototype solvers
  Based on Boolean decomposition
    A. Q. Dao, N.-Z. Lee, L.-C. Chen, M. P.-H. Lin, J.-H. R. Jiang, A. Mishchenko, and R. Brayton, "Efficient computation of ECO patch functions", Proc. DAC'18.
  Based on exact synthesis
    W. Haaswijk, M. Soeken, A. Mishchenko, and G. De Micheli, "SAT-based exact synthesis: Encodings, topology families, and parallelism", IEEE Trans. CAD, Vol. 39(4), April 2020, pp. 871-884.
  Based on the transduction method
    Y. Miyasaka, “Transduction method for AIG minimization”, Proc. IWLS’23, https://people.eecs.berkeley.edu/~alanmi/publications/2023 /iwls23_yukio.pdf
SRC Select Disclosure

## Slide 17: Transduction: Transformation + Reduction
Reduction
  If a wire is 0, 1, or don’t-care, it is replaced by a constant
Transformation
  Adding a fanin without changing the primary output function
    Functions and don’t-cares in the circuit may change
    The reduction performed next is based on the new don’t-cares
We use multi-input (not only two-input) AND gates
  N-input AND gate is decomposed into (N-1) 2-input AND gates
  At the tech-independent level, inverters are assumed to be free
The method was originally proposed in 1989
  S. Muroga, Y. Kambayashi, H. C. Lai and J. N. Culliney, "The transduction method-design of logic networks based on permissible functions," IEEE Trans. Comp, 1989, Vol. 38(10), pp. 1404-1424.
SRC Select Disclosure

## Slide 18: Experiments
In this presentation, we report the results on the last item (the transduction method) as these are more significant
To evaluate transduction, we used 94 (out of 100) test-cases from the logic syntethesis competition at IWLS’22
The results pass equivalence checking
The runtime ranges from minutes to hours
  Breaking news: a 5x speedup is achieved on 10 cores!
IWLS 2022 Programming Contest
  https://github.com/alanminko/iwls2022-ls-contest
The goal was to synthesize the smallest known circuits for 100 test-cases, without a runtime limit
SRC Select Disclosure

## Slide 19: Results
19
Benchmark | IWLS best | N=0 | N=20 | N=40 | N=100
ex00 | 23 | 23 | 21 | 21 | 21
ex01 | 27 | 24 | 24 | 24 | 23
ex03 | 24 | 25 | 25 | 25 | 24
ex05 | 39 | 40 | 38 | 37 | 37
ex10 | 10 | 10 | 10 | 10 | 10
ex11 | 20 | 20 | 20 | 20 | 20
ex12 | 30 | 30 | 30 | 30 | 30
ex13 | 46 | 47 | 44 | 44 | 42
ex14 | 63 | 60 | 60 | 58 | 58
ex16 | 18 | 18 | 18 | 18 | 18
ex17 | 24 | 24 | 24 | 24 | 24
ex18 | 32 | 32 | 32 | 32 | 32
ex19 | 38 | 38 | 38 | 38 | 38
ex20 | 56 | 53 | 52 | 49 | 49
ex21 | 70 | 62 | 58 | 58 | 56
Total | 520 | 506 | 494 | 488 | 482
Blue cells are ties
Green cells are wins
Red cells are losses
ex00-05:
Random functions
ex10-14:
Majority functions
ex16-21:
Sorting functions
SRC Select Disclosure

## Slide 20: Results (continued)
20
Benchmark | IWLS best | N=0 | N=20 | N=40 | N=100
ex50 | 18 | 18 | 18 | 18 | 18
ex51 | 29 | 26 | 26 | 26 | 26
ex52 | 19 | 19 | 18 | 18 | 18
ex53 | 40 | 36 | 36 | 34 | 34
ex54 | 12 | 12 | 12 | 12 | 12
ex56 | 29 | 29 | 29 | 29 | 29
ex60 | 67 | 60 | 56 | 55 | 53
ex62 | 40 | 40 | 40 | 40 | 40
ex92 | 29 | 29 | 29 | 29 | 29
ex93 | 41 | 41 | 39 | 39 | 39
ex94 | 36 | 34 | 33 | 33 | 33
ex95 | 65 | 61 | 59 | 59 | 58
ex97 | 69 | 61 | 57 | 56 | 55
Subtotal | 494 | 466 | 452 | 448 | 444
Total | 1461 | 1414 | 1381 | 1368 | 1357
Blue cells are ties
Green cells are wins
Red cells are losses
ex50-62:
Arithmetic functions
ex92-97:
Neuron functions
The complete results can be found in the paper https://people.eecs.berkeley.edu/~alanmi/publications/2023 /iwls23_yukio.pdf (https://app.pillar.science/datasets/189845)
SRC Select Disclosure

## Slide 21: Discussion
The proposed method outperformed the virtual best solver of IWLS 2022 Programming Contest
  23 wins, 61 ties, and remarkably no losses
One run took < 5 min (100 runs took < 9h)
Restarting from scratch with different parameters (randomized) improved the results
The reason why transduction works well
  Implemented on a minimalistic data-structure
  Uses the complete don’t-cares at each node
  Explores the search space using a stochastic approach
SRC Select Disclosure

## Slide 22: Recent Publications
22
Truth table based synthesis with don’t-cares
- Y. Miyasaka, A. Mishchenko, J. Wawrzynek, and N. J. Fraser, "Synthesizing practical Boolean functions using truth tables", Proc. IWLS'22.
- Y. Miyasaka. “Transduction method for AIG minimization”, Proc. IWLS’23, submitted to ICCAD’23.
Boolean decomposition and mapping
- A. Mishchenko, R. Brayton, A. T. Calvino, and G. De Micheli, "Boolean decomposition revisited", Submitted to Proc. IWLS'23.
- A. Mishchenko, R. Brayton, and M. Fujita, "Mapping and retiming revisited", Submitted to Proc. IWLS'23.
Infrastructure development and evaluation
- B.L.C. Barzen, A. Reais-Parsi, E. Hung, M. Kang, A. Mishchenko, J. W. Greene, and J. Wawrzynek, "Narrowing the synthesis gap: Academic FPGA synthesis is catching up with the industry", Proc. DATE'23.
SRC Select Disclosure
Notes: 22

## Slide 23: Conclusions
23
Reviewed the SRC task (first year)
“Standardizing Boolean transforms to improve quality and runtime of CAD tools”
Discussed ongoing work
Reviewed recent publications
SRC Select Disclosure
Notes: 23