## Slide 1: Golden Gate Bridging The Resource-Efficiency Gap Between ASICs and FPGA Prototypes
Albert Magyar, David Biancolin, Jack Koenig, Sanjit Seshia, Jonathan Bachrach, Krste Asanović

## Slide 2: Two major challenges of FPGA simulation
Labor-intensive
Chip might not fit
FireSim
Karandikar et al., “FireSim: FPGA-Accelerated Cycle-Exact Scale-Out System Simulation in the Public Cloud,” ISCA ‘18.

## Slide 3: FireSim: The easy button for FPGA simulation
Target Architecture
Target Microarchitecture
Simulator Microarchitecture
FPGA Implementation
Host FPGA Platform
Target Workloads
Golden Gate Compiler
Flexible SoC generators
User accelerator designs
Architectural experiments
“Batteries included” for the full stack!

## Slide 4: Two major challenges of FPGA simulation
Labor-intensive
Chip might not fit

## Slide 5: Why the chip won’t fit
Common ASIC structures map poorly
  Highly-ported RAMs
  Content-addressable memories
  Multiplexers
Abundant memory resources are underutilized
  Logic is relatively more expensive
Making the chip fit often means buying bigger FPGA!

## Slide 6
How do we make the chip fit?
Golden Gate: an optimizing compiler for simulators

## Slide 7: Golden Gate: a hardware compiler framework
Operating on concrete RTL target designs
Producing cycle- and bit-exact FPGA simulators
…structured as a network of communicating actors
…relying on decoupling to ease per-cycle synchronization
With a reusable API for FPGA-centric resource optimizations
With a basic optimization, we fit 50% more out-of-order cores per FPGA!

## Slide 8
Introduction
Prior work in increasing FPGA capacity
Golden Gate: an optimizing compiler for FPGA simulators
Case study: adding an optimization to Golden Gate
Verification of complex simulation models
Conclusion

## Slide 9
Introduction
Prior work in increasing FPGA capacity
Golden Gate: an optimizing compiler for FPGA simulators
Case study: adding an optimization to Golden Gate
Verification of complex simulation models
Conclusion

## Slide 10: Partitioning to solve capacity “cliffs”
Split design across multiple FPGAs
Each FPGA is still under-utilized!
Well put in HAsim†: “in order to maximize capacity of the multi-FPGA scenario we must first maximize utilization of an individual FPGA.”
† Pellauer et al., “HAsim: FPGA-Based High-Detail Multicore Simulation Using Time-Division Multiplexing” in HPCA 2011.

## Slide 11: Decoupling
FPGA prototype: one host FPGA clock = one simulated cycle
Decoupled simulator: target and host time advance independently
  Each target cycle may take multiple FPGA host cycles to simulate
Software RTL simulators take this idea to the extreme

## Slide 12: Clock gating: the simplest form of decoupling
input
output
clk
valid

## Slide 13: You can save resources with decoupling
Efficient 1-Read, 1-Write RAM
Resource-hogging
4-Read, 4-Write RAM
With 4 host cycles to simulate 1 target cycle ➨ trade space for time!

## Slide 14: Tradeoff: it now takes 4 host cycles to simulate one target cycle, but we save FPGA resources

## Slide 15: Decoupling enables optimizations that can significantly reduce utilization
No tools to apply them automatically

## Slide 16: Where prior work falls short
Target Architecture
Target Microarchitecture
Simulator Microarchitecture
FPGA Implementation
Host FPGA Platform
Target Workloads
Paper idea: conceptual improvement in simulator architecture and/or microarchitecture arch
Paper artifact: “artisanal” simulator based on idea
Different goals: why write a compiler for RTL if most users don’t have working RTL to start with?
PhD student cleverness
Conceptual simulation stack

## Slide 17
Introduction
Prior work in increasing FPGA capacity
Golden Gate: an optimizing compiler for FPGA simulators
Case study: adding an optimization to Golden Gate
Verification of complex simulation models
Conclusion

## Slide 18: A compiler framework for FPGA simulators
Target RTL
Optimized, decoupled simulator
Guarding state updates
Transforming costly RAMs
Multi-threading host logic
These compiler passes are not RTL-preserving
The generated simulator no longer implements the target’s RTL semantics
But it must simulate them in a cycle-exact manner!
Golden Gate Compiler

## Slide 19: Building blocks for Golden Gate
Strong model of simulator behavior
Infrastructure for hardware compiler development
Interface
Implementation
Latency-Insensitive Bounded Dataflow Networks [1]
FIRRTL: Flexible Intermediate Representation for RTL [2]
[1] Vijayaraghavan et al., “Bounded Dataflow Networks and Latency-Insensitive Circuits,” MEMOCODE ‘09.
[2] Izraelevitz et al., “Reusability is FIRRTL Ground: Hardware Construction Languages, Compiler Frameworks, and Transformations,” ICCAD ’17.

## Slide 20: Golden Gate models simulator as a dataflow network
Dividing target into multiple models enables composable optimizations!
Optimized Mapping
Un-optimized Mapping
Simulation Collateral

## Slide 21: Latency-Insensitive Bounded Dataflow Networks*
General design technique to avoid synchronous design constraints
Replace synchronously timed signals with decoupled channels
BDNs: Bounded Dataflow Networks
Latency-Insensitive BDNs (LI-BDNs)
Conform to a set of properties on both token values and the conditions under which tokens must be produced/accepted
As a simulator: properties prescribe the behavior of tokens modeling inputs and outputs of components that are simulated.
* Vijayaraghavan et al., “Bounded Dataflow Networks and Latency-Insensitive Circuits,” MEMOCODE ‘09.

## Slide 22: Compiler pass: RTL block to unoptimized LI-BDN
Model the value of a given I/O on a particular cycle with a token
Replace I/O with token queues
Analyze netlist to find combinational I/O dependencies
Transform RTL to a set of guarded atomic actions
  Update target state when per-cycle synchronization is complete
  I/O tokens are processed according to LI-BDN properties

## Slide 23: LI-BDN structure guarantees freedom from deadlock and defines equivalence of two simulator components!
Helpful framework for inserting resource-optimized simulator components!

## Slide 24: Building blocks for Golden Gate
Interface
Implementation
Latency-Insensitive Bounded Dataflow Networks [1]
FIRRTL: Flexible Intermediate Representation for RTL [2]
[1] Vijayaraghavan et al., “Bounded Dataflow Networks and Latency-Insensitive Circuits,” MEMOCODE ‘09.
[2] Izraelevitz et al., “Reusability is FIRRTL Ground: Hardware Construction Languages, Compiler Frameworks, and Transformations,” ICCAD ’17.

## Slide 25: FIRRTL hardware compiler framework (ICCAD ‘17)
Extensive suite of tools for writing hardware compiler passes
Aimed at helping separate RTL from low-level implementation details
Makes writing CAD tools for chip design accessible to a wide audience!

## Slide 26: Golden Gate is structured as an extensible compiler
Sequence of FIRRTL passes
Optimizations fit in reusable framework

## Slide 27
Introduction
Prior work in increasing FPGA capacity
Golden Gate: an optimizing compiler for FPGA simulators
Case study: adding an optimization to Golden Gate
Verification of complex simulation models
Conclusion

## Slide 28: Case study: implementing an optimizing transform
Application: optimizing highly-ported register files in BOOM, an open-source RISC-V out-of-order core for the Rocket Chip Generator

## Slide 29: The Rocket Chip Generator
Parameterizable SoC Generator [1]
Cache-coherent TileLink network
Variable number of cores
                Rocket: 5-stage in-order
BOOM: parameterized out-of-order [2]
[1] Asanović et al., “The Rocket Chip Generator,” Berkeley Tech Report, 2016.
                [2] Celio et al. “The Berkeley Out-of-Order Machine (BOOM): An Industry-Competitive, Synthesizable, Parameterized RISC-V Processor,” Berkeley Tech Report, 2015.

## Slide 30: How the multi-ported memory optimization works
Create multi-model simulator hierarchy
Extract memory that is problematic for QoR
Generate an FPGA-optimized memory model
  Models exact target memory
  Resource-efficient underlying BRAM
Mapped independently from rest of circuit

## Slide 31: How do we know this optimization works?
While FPGA simulation helps with pre-silicon verification, it brings new challenges.
A functional bug in the simulator can manifest as:
An apparent functional bug in the target
A timing irregularity in the target
Nondeterminism of execution or host deadlock
LIME: Automatic checking of decoupled models

## Slide 32: LIME: Automatic checking of decoupled models
Checks LI-BDN properties with BMC
Ensures model is cycle-accurate
Targets UCLID5 modeling system
Used to verify multi-port RAM model
Inputs: reference RTL & model RTL Output: counterexample waveforms (if any)

## Slide 33: Results of optimizing register files
BOOM
BOOM
BOOM
BOOM
BOOM
BOOM
VU9P FPGA
Same VU9P FPGA
4 cores ➨6 cores
Underlying 1R1W implementation maps efficiently to FPGA block RAMS (BRAMs)

## Slide 34: Results of optimizing register files
FPGA resource utilization on Xilinx VU9P FPGAs (AWS F1 devices)
Rx = x Rocket cores, By = y BOOM cores
33% less LUT utilization per core
Ample slack in BRAM count

## Slide 35: Future work: multi-threading to save resources
Why not borrow from software simulators and time-multiplex one copy of host logic to simulate N copies of a target block?
[1] Z. Tan et al, “RAMP Gold : A High-Throughput FPGA-Based Manycore Simulator,” DAC ‘10.
[2] M. Pellauer et al., “HAsim: FPGA-Based High-Detail Multicore Simulation Using Time-Division Multiplexing,” HPCA ‘12.
[3] Z. Tan et al., “A Case for FAME: FPGA Architecture Model Execution,” ISCA ‘10.

## Slide 36
Introduction
Prior work in increasing FPGA capacity
Golden Gate: an optimizing compiler for FPGA simulators
Case study: adding an optimization to Golden Gate
Verification of complex simulation models
Conclusion

## Slide 37: Conclusion
We present Golden Gate, a compiler framework for FPGA simulators
It includes a spec for simulators structured as dataflow networks
We provide an API for heterogenous compiler passes
Golden Gate open-sourced as part of FireSim @ https://fires.im
As a case study, we present a multi-cycle RAM optimization that significantly increases simulation capacity of a large Xilinx FPGA!