University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Fall 2000

Solution Set # 5

- In lecture, we briefly presented a design for a negative edge-triggered D flip-flop.

- Create a timing diagram that illustrates the potential problems that happen when the data input D changes (too) close to the falling edge. That is, illustrate a situation in which the input change is not latched by the flip-flop.

CLK

D

Q

D transitions too close to the falling edge, and the high value is not latched.  The D input is seen only after another falling edge occurs.

- Modify the design of the flip-flop to make it positive edge-triggered. Include a timing waveform that illustrates how your flip-flop implementation works.

Q

CLK

Q’

D

CLK

D

Q

- Add to the negative edge-triggered flip-flop the inputs R (Reset) and S (Set). When the former is asserted, independent of the clock, the flip-flop state is forced to zero. When Set is asserted, the state is forced to one.

R

Q

CLK

Q’

S

D

- Modify your answer to part (c) so that the Rest and Set input only take effect on the falling edge of the clock.

Q

CLK

Q’

S

D

R’

- In lecture, we presented a Master-Slave flip-flop.

- How would you add asynchronous (i.e., independent of the clock) set and reset signals to initialize the flip-flop to a one or zero respectively?

- Master-Slave flip-flops exhibit the phenomena of “ones catching.” Explain what it is and why it happens. Is it possible for a Master-Slave flip-flop to “catch zeros”? Justify your answer!

An RS latch is made of two NOR gates that hold state when the inputs are 0.  If Set transitions to 1 then it gets set.  If it subsequently transitions back to 0 it is still set at 1.  If the Set glitches and jumps to 1 and then back to 0 quickly the 1 will still be held by the latch.  It catches the one even though it may be a quick transition.

A flipflop may catch zeros if it is made of NAND gates where 1’s will make the latch hold state and a zero will set the latch.  If there is a glitch, the latch may catch a zero, therefore it is possible for a Master-Slave flip-flop to do “zeros catching.”

3) The circuit shown below can be used as a debouncer. Once the switch is set to S, the output will become high. Then, even if the switch disconnects with S the output will keep its current value.

The timing diagram shown below shows the circuit’s behavior:

4a)  Q+ = Q XOR T

| Q | T | Q+ |
| --- | --- | --- |
| 0 | 0 | 0 |
| 0 | 1 | 1 |
| 1 | 0 | 1 |
| 1 | 1 | 0 |

4b)    JK: 			T = JQ’ + KQ

| J | K | Q | Q+ | T |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 1 |
| 1 | 0 | 0 | 1 | 1 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 0 | 1 |

D:				T = D XOR Q

| D | Q | Q+ | T |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 1 |
| 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 |

5a) X = D ; Y = Q

| D | Q | Q+ | X | Y |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 1 | 1 | 1 |

5b) X = T XOR Q ; Y = Q

| T | Q | Q+ | X | Y |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 1 | 1 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 1 |

5c) X = J + Q ; Y = K’Q

| J | K | Q | Q+ | X | Y |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 | 1 | 1 |
| 0 | 1 | 0 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 1 | 1 | 0 |
| 1 | 0 | 1 | 1 | 1 | 1 |
| 1 | 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 1 | 0 | 1 | 0 |

# Text boxes

R	    Q’

S	     Q

Q

Q’

S

R

K

J

CLK

R	    Q’

S                 Q